## Slide 1: Flexibly configuring task and motion planning problems for mobile manipulators
Siddhant Saoji and Jan Rosell
Department of Mechanical Engineering
Institute of Industrial and Control Engineering

## Slide 2: Problem statement and proposed solution
This paper presents a TAMP framework that includes an easy way to configure the interconnection between planning layers.
Mobile manipulators face different problems at the perception, planning and control levels.
task planning / motion planning

## Slide 3: The motion planning server and the task planning server
Motion planning problems are modeled using an XML file with information on the models of the robot(s) and obstacles, the controls and the planner.
OpenProblem / CloseProblem
SetRobotsConfig / GetObstaclePos / SetObstaclePos
AttachObstacle2RobotLink / DetachObstacle
SetPlannerByName / SetQuery / GetPath
Some ROS services provided are:

## Slide 4: The motion planning server and the task planning server
The Fast Forward task planner has been wrapped as a ROS service that:
  Uses PDDL domain and problem files as request
  Returns the sequence of actions as a vector of strings

## Slide 5: Interfacing layers proposal and the TAMP client
An XML file has been conceived as the intermediate layer for the flexible linkage between:
  symbolic actions and
  geometric data

## Slide 6: Interfacing layers proposal and the TAMP client
The TAMP configuration file includes the files:
  the PDDL domain and problem files
  the Kautham problem file

## Slide 7: Interfacing layers proposal and the TAMP client
The TAMP configuration file includes information on the initial state:
  Objects to be manipulated and their poses
  Robots, their control files and the controls values that define the robot initial configuration

## Slide 8: Interfacing layers proposal and the TAMP client
The TAMP configuration file includes information linking the symbols involved in the PDDL Actions with the required geometric information to plan the motions that may allow to actually perform those actions.
  Pick
  Place
  Move

## Slide 9: Interfacing layers proposal and the TAMP client
Initialization

## Slide 10: Interfacing layers proposal and the TAMP client
Task planning

## Slide 11: Interfacing layers proposal and the TAMP client
Motion planning (Pick)

## Slide 12: Interfacing layers proposal and the TAMP client
Motion planning (Place)

## Slide 13: Interfacing layers proposal and the TAMP client
Motion planning (Move)

## Slide 14: An example, discussion and future work

## Slide 15: An example, discussion and future work
XML file is currently configured by hand, and the challenge is to automatically:
  set the initial state by using deep learning vision techniques
  set the PDDL problem file using reasoning procedures and ontological knowledge
  generate action oriented grasp configurations, using learning techniques and a grasp generator
The framework presented gives the tools:
to get easy access to task and motion planning servers, and
to easily set manipulation problems through the simple interconnection between planning layers using an XML file

## Slide 16: Flexibly configuring task and motion planning problems for mobile manipulators
Siddhant Saoji and Jan Rosell